## Slide 1: 신호 최적화 최종발표
ETRI연구연수생 강민수

## Slide 2: Contents
Current Model
  3x3Grid Single-Agent Model without Restraints(Depreciated)
  3x3Grid Decentralized Model without Restraints(Depreciated)
  3x3Grid Decentralized Model with Practical Restraints
  Dunsan Decentralized Model with Practical Restraints
  Dunsan Decentralized CNN Model with Practical Restraints
Upcoming Model
  Continuous Action Model with practical restraints

## Slide 3: 3x3Grid Single-Agent/Decentralized Model without Restraints(Depreciated)
Condition (seed fixed)
  Generating probability 0.133 (left, right), 0.388 (up, down)
  Restricted direction of vehicles(via)/Not restricted direction(no via)
  Central agent(n_1_1), 9 Agents(decentralized)
State
  The number of inflow vehicles from each inflow edge(left, straight)
Action
  Deciding next phase(without an order), every 20s (with all yellow 3 seconds)
Reward
  Penalty on Pressure (= inflow-outflow)

## Slide 4: Comparison between Simulation & Single Agent
Simulation 0.133 (left, right), 0.388 (up, down), phase 42(G), 3(Y)
  The number of arrived number: 8295 (no via), 8794 (via)
Experiment(Single-Agent Model)
  The number of average arrived number: 9060 (no via), 9281 (via)
Agent
5~8% Increase
300m

## Slide 5: Comparison between Simulation & Decentralized Agents
Simulation 0.133 (left, right), 0.388 (up, down), phase 20(G), 3(y)
  The number of arrived number: 9474 (no via), 9765(via)
Experiment(Decentralized Agents Model)
  The number of avg arrived number: 10600(no via, blue), 10800 (via, orange)
10~11% Increase

## Slide 6: 3x3Grid Decentralized Model with Practical Restraints
Condition(seed fixed)
  Random routing vehicle generation (period 0.8), scale 1.1 (by randomTrips.py)
  9 Decentralized Agents(No offsets, Update Asynchronously)
  4 Phases(Vertical/Horizontal straight and left) 37s each, followed by all yellow 3s
  Model applied min/max duration(28s,49s) and phase period(160s)
State
  The number of inflow vehicles from each inflow edge(left, straight)
  Update current phase demand info from end of current phase

## Slide 7: 3x3Grid Decentralized Model with Practical Restraints
Action
  Common phase-based ratio discrete distribution
  2 Actions/agent = time action, rate action
Action Space
  Time action space:
  Rate action space: 18, distributing time action ex) [0,1,0,-1],[0,0,0,0],[1,1,-1,-1]
Reward
  Reward= -Pressure = (inflow HaltingNumber – outflow VehicleNumber)
  If action is beyond the threshold(min/max duration), give penalties
  Update end of phase period

## Slide 8: 3x3Grid Decentralized Model with Practical Restraints